## Slide 1
ARDUINO
WORKSHOP 1
Build a responsive LED controller with the circuit and code together.
ENGN 3340 / SUCCESS CENTRE

## Slide 2
ENGN 3340 / SUCCESS CENTRE
WHAT I NOTICED
Most people wired the LEDs. The harder part was making the code respond to inputs reliably.
Today: one circuit, one growing sketch, one new problem at a time.

## Slide 3
ENGN 3340 / SUCCESS CENTRE
OUR HARDWARE
The workshop uses a Mega. Tinkercad uses an Uno, so only the pin numbers change.
Mega D2 to GND; internal pull-up.
One button
Mega D22–D29, one resistor per LED.
Eight LEDs
5 V, GND and the A0 wiper.
One pot
Arduino Mega 2560 Rev3 pinout, Arduino (CC BY-SA 4.0).

## Slide 4
ENGN 3340 / SUCCESS CENTRE
THE CIRCUIT
Follow the wires before reading the code. The Tinkercad build uses an Uno; the workshop sketches use a Mega.
Workshop Tinkercad circuit, supplied by Kelenna.
UNO PIN MAP
D9–D2: eight LEDs, one resistor each D10: button to GND A0: potentiometer wiper
Mega sketch: D22–D29 LEDs · D2 button · A0 pot

## Slide 5
ENGN 3340 / SUCCESS CENTRE
KEEP PINS 0 AND 1 FREE
D0/RX0 and D1/TX0 carry USB Serial. Using them for LEDs or buttons can confuse uploads and the Serial Monitor.
Mega: D22–D29 LEDs, D2 button, A0 pot.
Use the planned pins
Released reads HIGH; pressed reads LOW.
INPUT_PULLUP
Check polarity, series resistor and common GND.
LED current path
Rails may be split. Check continuity before debugging code.
Breadboard rails
01
02
03
04
Code link: https://github.com/KelennaUdo/Arduino-Session

## Slide 6
ENGN 3340 / SUCCESS CENTRE
SKETCH STRUCTURE
setup() runs once. loop() repeats while the board is powered.
SKETCH STRUCTURE
void setup() { Serial.begin(9600); // Configure pins here. } void loop() { // Read, decide and update. }
Notes: Sketch 01

## Slide 7
ENGN 3340 / SUCCESS CENTRE
SETTING PINS
pinMode() tells a digital pin whether to receive or drive a signal.
SETUP
pinMode(buttonPin, INPUT_PULLUP); for (int i = 0; i < ledCount; i++) { pinMode(ledPins[i], OUTPUT); }
Notes: Sketch 01

## Slide 8
ENGN 3340 / SUCCESS CENTRE
DIGITAL INPUT
With INPUT_PULLUP, released is HIGH (1) and pressed is LOW (0). Check both in Serial Monitor.
DIGITAL INPUT
bool buttonState = digitalRead(buttonPin);
Serial.print("button = ");
Serial.println(buttonState);
Notes: Sketch 01

## Slide 9
ENGN 3340 / SUCCESS CENTRE
ANALOG INPUT
(POTENTIOMETER)
Analog input converts the wiper voltage into a value from 0 to 1023.
ANALOG INPUT
int potValue = analogRead(potPin); Serial.println(potValue); // Turn the knob. What changes?
Notes: Sketch 01

## Slide 10
ENGN 3340 / SUCCESS CENTRE
ARRAYS
An array groups the LED pins; currentLed selects an index from 0 to 7. Sketch 02 calculates ledCount from the array; later sketches set it to 8.
VARIABLE + ARRAY
const int ledPins[] = { 22, 23, 24, 25, 26, 27, 28, 29 }; const int ledCount = 8; int currentLed = 0;
Notes: Sketch 02

## Slide 11
ENGN 3340 / SUCCESS CENTRE
FUNCTIONS AND FOR LOOPS
A function is a self-contained, reusable block of code designed to perform a specific task
This function:
Sets every LED LOW
Then sets only the current LED HIGH
FUNCTION + FOR LOOP
void showLed() {
for (int i = 0; i < ledCount; i++) {
digitalWrite(ledPins[i], LOW);
}
digitalWrite(ledPins[currentLed], HIGH);
}
Notes: Sketch 02

## Slide 12
ENGN 3340 / SUCCESS CENTRE
ANOTHER FUNCTION
Increment the current LED index to the next LED. After index 7, start again at 0.
Note ledCount = 8
FORWARD SEQUENCE
void advanceLed() { currentLed++; if (currentLed >= ledCount) { currentLed = 0; } showLed(); }
Notes: Sketch 03

## Slide 13
ENGN 3340 / SUCCESS CENTRE
MAKE IT MOVE
with delay()
The LED moves, but a short button press may be missed while delay(500) blocks loop().
BLOCKING
delay(500); advanceLed();
OBSERVE
// Tap the button briefly. // Was it seen?
Notes: Sketch 03

## Slide 14
ENGN 3340 / SUCCESS CENTRE
CHECK TIME WITH millis()
The loop keeps reading inputs. The LED advances only after enough time has elapsed.
NO DELAY()
unsigned long now = millis(); if (now - previousStep >= interval) { previousStep = now; advanceLed(); }
Notes: Sketch 04

## Slide 15
ENGN 3340 / SUCCESS CENTRE
POTENTIOMETER SETS THE SPEED
A higher reading gives a shorter interval.
ADC VALUE TO MILLISECONDS
int potValue = analogRead(potPin); interval = map(potValue, 0, 1023, 1000, 100);
Notes: Sketch 05

## Slide 16
ENGN 3340 / SUCCESS CENTRE
DEBOUNCE
THE BUTTON
A button can briefly flicker between HIGH and LOW. Accept its new value after it stays steady for 30 ms.
Each new reading that’s different than the previous restarts a 30-ms timer.
Restart timer
Update stableButton with the new value if they are different, and if the 30 ms timer passes (meaning the new reading was the same), then
do the thing.
Accept change
01
02
STABLE CHANGE
if (reading != lastReading)
buttonChangedAt = now;
if (now - buttonChangedAt >= 30 &&
reading != stableButton) {
stableButton = reading;
}
lastReading = reading;
stableButton is a variable.
It will store only the button’s stable value.
Notes: Sketch 05

## Slide 17
ENGN 3340 / SUCCESS CENTRE
TOGGLE
RUN / PAUSE
Only a settled LOW is a press. A settled HIGH records the release without toggling again.
The ! operator flips a bool: RUN becomes PAUSE, and PAUSE becomes RUN.
Press event
When resuming, start a full LED interval from now.
Resume timing
01
02
INSIDE THE 30 ms CHECK
if (stableButton == LOW) {
running = !running;
if (running) previousStep = now;
}
Notes: Sketch 05

## Slide 18
BUTTON ALGORITHM
Notes: Sketch 05

## Slide 19
ENGN 3340 / SUCCESS CENTRE
DEBUG ONE THING AT A TIME
When things behave strangely, compare the value you expect with the value you actually read.
Released HIGH, pressed LOW?
Button
Does ADC change from near 0 to 1023?
Pot
Does interval change between 1000 and 100 ms?
Timing
Does currentLed stay between 0 and 7?
Output
01
02
03
04
SERIAL MONITOR
Serial.print("LED = "); Serial.print(currentLed); Serial.print(" interval = "); Serial.println(interval);
Notes: Sketch 05

## Slide 20
ENGN 3340 / SUCCESS CENTRE
SCANNER CHALLENGE
Make the light travel 0, 1, ... 7, 6, ... 0.
Keep the potentiometer for speed, the button for RUN/PAUSE and millis().
//hint: What else must the Arduino remember in the function below?
void advanceLed() {
// TODO: bounce at each end.
currentLed++;
if (currentLed >= ledCount) currentLed = 0;
showLed();
}
Notes: Sketch 05

## Slide 21
ENGN 3340 / SUCCESS CENTRE
BEFORE YOU LEAVE
Good and detailed coding tutorials:
https://www.youtube.com/watch?v=BLrHTHUjPuw&t=64s
https://www.youtube.com/watch?v=zJ-LqeX_fLU&t=1706s